Physics 3204

Assignment #5: Electrostatics and Electric Fields

- Sphere #1 has a charge of +2q and sphere #2 has a charge of +6q.  The force between them is 0.003 N.  They are simultaneously touched by a third identical sphere with a charge of -2q.  After the third sphere is removed, spheres #1 and #2 are placed in their original positions.  What is the new force between them?

- What must be the distance between two 5.0 μC charges if the electrostatic force between them is 5.0 x 10-2 N?

- Three charges are arranged in a triangle as shown below.  If the charge on A is +1.00 μC, the charge on B is -3.50 μC and the charge on C is -2.00 μC, find the net force on B.

- What is the electric field strength at midway between charged objects of +4.70 μC and -3.20 μC that are placed 80.0 cm apart?

- At a certain point in an electric field, a charge of 2.0 μC has an electric potential energy of 18 J.  What would be the electric potential energy at the same point for a charge of 6.0 μC?

- At a point 12 cm from a point charge the electric potential is 12.0 V.  What will be the potential 6.0 cm away?

- A proton is moved through a potential difference of 110 V.  How much work is done?

- A proton that is initially at rest is accelerated through an electric potential difference of 400 V.  What is the speed of the proton?

- An atomic particle with a mass of 5.2 x 10-9 kg and an initial speed of 3.0 x 103 m/s is fired at a stationary charge of 4.0 x 10-10 C that is 5.0 mm away.  If the moving particle has a charge of 2.0 x 10-10 C, how close to the stationary charge will it be when it finally stops and reverses direction?

# Text boxes

25.0 cm

15.0 cm

C

B

A