Physics 3204

Electricity

For each circuit shown below, find the current and voltage through each resistor.

1.

2.

3.

4.

5.  This graph shows the relationship between measurements of V and I for two different loads. Which load has the greater resistance? Explain.

6.  Two light bulbs are connected to a source in an electrical circuit. Explain what would happen if one of the bulbs burned out, if the bulbs were connected:

(A)		in parallel with one another

- in series with one another

7.  How much work is done on 10.0 C of charge to move it through a potential difference of 9.0 V in 10.0 s?

8.  What is the potential difference of a battery if it provides 250 J of energy to a load in a 12.0 A circuit in 2.3 s?

9.  A toy train set has a resistance of 20.0  and uses a current of 250 mA. If it ran for

one hour, what is the power of the train?

10.  An electric toaster draws 5.00 A from a 120-V outlet for 3.0 h. If electricity costs 9.90¢ per kilowatt hour, what is the total cost?

11.  A wire has a resistance of 0.50 .  What is the resistance of the wire if the length has been tripled and the diameter of the wire has been cut in half?

# Text boxes

R1 = 12 Ω

R3 = 2.2 Ω

R2 = 6.4 Ω

VT = 34 V

R1 = 120 Ω

R2 = 240 Ω

R3 = 360 Ω

VT = 28 V

VT = 48 V

R1 = 46 Ω

R5 = 32 Ω

R2 = 75 Ω

R4 = 125 Ω

R3 = 95 Ω

R1 = 41 Ω

R4 = 130 Ω

R2 = 110 Ω

R3 = 205 Ω

VT = 72 V